## OV5640 SENSOR INFORMATION
optical size of 1/4"
automatic image control functions: automatic exposure control (AEC), automatic white balance (AWB), automatic band filter (ABF), automatic 50/60 Hz luminance detection, and automatic black level calibration (ABLC)
programmable controls for frame rate, AEC/AGC 16-zone size/position/weight control, mirror and flip, cropping, windowing, and panning
image quality controls: color saturation, hue, gamma, sharpness (edge enhancement), lens correction, defective pixel canceling, and noise canceling
support for output formats: RAW RGB, RGB565/555/444, CCIR656, YUV422/420, YCbCr422, and compression
support for video or snapshot operations
support for horizontal and vertical sub-sampling, binning
digital video port (DVP) parallel output interface and dual lane MIPI output interface
support for images sizes: 5 mega pixel, and any arbitrary size scaling down from 5 mega pixel
support for auto focus control (AFC) with embedded AF VCM driver
active array size:2592 x 1944
power supply: / core: 1.5V ± 5% (with embedded 1.5V regulator) / analog: 2.6 ~ 3.0V (2.8V typical), / I/O: 1.8V / 2.8V
Input clock frequency:6~27 MHz
maximum image transfer rate: / QSXGA (2592x1944): 15 fps / 1080p: 30 fps / 1280x960: 45 fps / 720p: 60 fps / VGA (640x480): 90 fps / QVGA (320x240): 120 fps
shutter: / rolling shutter / frame exposure

# OV5640 Sensor Driver
## Step 1: Kernel Version, Driver location
VERSION = 4
PATCHLEVEL = 19
SUBLEVEL = 0
EXTRAVERSION =

linux-xlnx-master/drivers/media/i2c/ov5640.c

## Step 2: Driver Register / Init function

static const struct i2c_device_id ov5640_id[] = {
{"ov5640", 0},
{},
};
MODULE_DEVICE_TABLE(i2c, ov5640_id);

static const struct of_device_id ov5640_dt_ids[] = {
{ .compatible = "ovti,ov5640" },
{ /* sentinel */ }
};
MODULE_DEVICE_TABLE(of, ov5640_dt_ids);

static struct i2c_driver ov5640_i2c_driver = {
.driver = {
.name = "ov5640",
.of_match_table	= ov5640_dt_ids,
},
.id_table = ov5640_id,
.probe = ov5640_probe,
.remove = ov5640_remove,
};

module_i2c_driver(ov5640_i2c_driver);

## Step 3: Probe function

static int ov5640_probe(struct i2c_client *client, const struct i2c_device_id *id)
{
struct device *dev = &client->dev;
struct fwnode_handle *endpoint;
struct ov5640_dev *sensor;
struct v4l2_mbus_framefmt *fmt;
u32 rotation;
int ret;

sensor = devm_kzalloc(dev, sizeof(*sensor), GFP_KERNEL);
if (!sensor)
return -ENOMEM;

sensor->i2c_client = client;

/*
* default init sequence initialize sensor to
* YUV422 UYVY VGA@30fps
*/
fmt = &sensor->fmt;
fmt->code = MEDIA_BUS_FMT_UYVY8_2X8;
fmt->colorspace = V4L2_COLORSPACE_SRGB;
fmt->ycbcr_enc = V4L2_MAP_YCBCR_ENC_DEFAULT(fmt->colorspace);
fmt->quantization = V4L2_QUANTIZATION_FULL_RANGE;
fmt->xfer_func = V4L2_MAP_XFER_FUNC_DEFAULT(fmt->colorspace);
fmt->width = 640;
fmt->height = 480;
fmt->field = V4L2_FIELD_NONE;
sensor->frame_interval.numerator = 1;
sensor->frame_interval.denominator =	ov5640_framerates[OV5640_30_FPS];
sensor->current_fr = OV5640_30_FPS;
sensor->current_mode =
&ov5640_mode_data[OV5640_30_FPS]	[OV5640_MODE_VGA_640_480];
sensor->last_mode = sensor->current_mode;

sensor->ae_target = 52;

/* optional indication of physical rotation of sensor */
ret = fwnode_property_read_u32(dev_fwnode(&client->dev), "rotation",
      &rotation);
if (!ret) {
switch (rotation) {
case 180:
sensor->upside_down = true;
/* fall through */
case 0:
break;
default:
dev_warn(dev, "%u degrees rotation is not supported, ignoring...\n",
rotation);
}
}

endpoint = fwnode_graph_get_next_endpoint(dev_fwnode(&client->dev), NULL);
if (!endpoint) {
dev_err(dev, "endpoint node not found\n");
return -EINVAL;
}

ret = v4l2_fwnode_endpoint_parse(endpoint, &sensor->ep);
fwnode_handle_put(endpoint);
if (ret) {
dev_err(dev, "Could not parse endpoint\n");
return ret;
}

/* get system clock (xclk) */
sensor->xclk = devm_clk_get(dev, "xclk");
if (IS_ERR(sensor->xclk)) {
dev_err(dev, "failed to get xclk\n");
return PTR_ERR(sensor->xclk);
}

sensor->xclk_freq = clk_get_rate(sensor->xclk);
if (sensor->xclk_freq < OV5640_XCLK_MIN ||
   sensor->xclk_freq > OV5640_XCLK_MAX) {
dev_err(dev, "xclk frequency out of range: %d Hz\n",
sensor->xclk_freq);
return -EINVAL;
}

/* request optional power down pin */
sensor->pwdn_gpio = devm_gpiod_get_optional(dev, "powerdown",
   GPIOD_OUT_HIGH);
/* request optional reset pin */
sensor->reset_gpio = devm_gpiod_get_optional(dev, "reset",
    GPIOD_OUT_HIGH);

v4l2_i2c_subdev_init(&sensor->sd, client, &ov5640_subdev_ops);

sensor->sd.flags |= V4L2_SUBDEV_FL_HAS_DEVNODE;
sensor->pad.flags = MEDIA_PAD_FL_SOURCE;
sensor->sd.entity.function = MEDIA_ENT_F_CAM_SENSOR;
ret = media_entity_pads_init(&sensor->sd.entity, 1, &sensor->pad);
if (ret)
return ret;

ret = ov5640_get_regulators(sensor);
if (ret)
return ret;

mutex_init(&sensor->lock);

ret = ov5640_check_chip_id(sensor);
if (ret)
goto entity_cleanup;

ret = ov5640_init_controls(sensor);
if (ret)
goto entity_cleanup;

ret = v4l2_async_register_subdev(&sensor->sd);
if (ret)
goto free_ctrls;

return 0;

free_ctrls:
v4l2_ctrl_handler_free(&sensor->ctrls.handler);
entity_cleanup:
mutex_destroy(&sensor->lock);
media_entity_cleanup(&sensor->sd.entity);
return ret;
}

## Step 4: struct v4l2_subdev_ops

static const struct v4l2_subdev_core_ops ov5640_core_ops = {
.s_power = ov5640_s_power,
};

static const struct v4l2_subdev_video_ops ov5640_video_ops = {
.g_frame_interval = ov5640_g_frame_interval,
.s_frame_interval = ov5640_s_frame_interval,
.s_stream = ov5640_s_stream,
};

static const struct v4l2_subdev_pad_ops ov5640_pad_ops = {
.enum_mbus_code = ov5640_enum_mbus_code,
.get_fmt = ov5640_get_fmt,
.set_fmt = ov5640_set_fmt,
.enum_frame_size = ov5640_enum_frame_size,
.enum_frame_interval = ov5640_enum_frame_interval,
};

static const struct v4l2_subdev_ops ov5640_subdev_ops = {
.core = &ov5640_core_ops,
.video = &ov5640_video_ops,
.pad = &ov5640_pad_ops,
};

## Step 5: ov5640_s_power

static int ov5640_s_power(struct v4l2_subdev *sd, int on)
{
        struct ov5640_dev *sensor = to_ov5640_dev(sd);
        int ret = 0;

        mutex_lock(&sensor->lock);

        if (sensor->power_count == !on) {
        ret = ov5640_set_power(sensor, !!on);
        if (ret)
        goto out;
        }

        /* Update the power count. */
        sensor->power_count += on ? 1 : -1;
        WARN_ON(sensor->power_count < 0);
out:
        mutex_unlock(&sensor->lock);
        return ret;
}

static int ov5640_set_power(struct ov5640_dev *sensor, bool on)
{
        int ret = 0;

        if (on) {
        ret = ov5640_set_power_on(sensor);
        if (ret)
        return ret;

        ret = ov5640_restore_mode(sensor);
        if (ret)
        goto power_off;

/*
        * Power up MIPI HS Tx and LS Rx; 2 data lanes mode
        *
        * 0x300e = 0x40
        * [7:5] = 010 : 2 data lanes mode (see FIXME note in
        * "ov5640_set_stream_mipi()")
        * [4] = 0 : Power up MIPI HS Tx
        * [3] = 0 : Power up MIPI LS Rx
        * [2] = 0 : MIPI interface disabled
        */
        ret = ov5640_write_reg(sensor,
        OV5640_REG_IO_MIPI_CTRL00, 0x40);
        if (ret)
        goto power_off;

        /*
        * Gate clock and set LP11 in 'no packets mode' (idle)
        *
        * 0x4800 = 0x24
        * [5] = 1 : Gate clock when 'no packets'
        * [2] = 1 : MIPI bus in LP11 when 'no packets'
        */
        ret = ov5640_write_reg(sensor,
        OV5640_REG_MIPI_CTRL00, 0x24);
        if (ret)
        goto power_off;
        /*
        * Set data lanes and clock in LP11 when 'sleeping'
        *
        * 0x3019 = 0x70
        * [6] = 1 : MIPI data lane 2 in LP11 when 'sleeping'
        * [5] = 1 : MIPI data lane 1 in LP11 when 'sleeping'
        * [4] = 1 : MIPI clock lane in LP11 when 'sleeping'
        */
        ret = ov5640_write_reg(sensor,
        OV5640_REG_PAD_OUTPUT00, 0x70);
        if (ret)
        goto power_off;

        /* Give lanes some time to coax into LP11 state. */
        usleep_range(500, 1000);
        }
}

        - -------------|
        |	|
Reset -------------------------| | --------------

      –---------
        | |
power dn | |------------------------------------

static void ov5640_power(struct ov5640_dev *sensor, bool enable)
{
        gpiod_set_value_cansleep(sensor->pwdn_gpio, enable ? 0 : 1);
}

static void ov5640_reset(struct ov5640_dev *sensor)
{
        if (!sensor->reset_gpio)
        return;

        gpiod_set_value_cansleep(sensor->reset_gpio, 0);

        /* camera power cycle */
        ov5640_power(sensor, false);
        usleep_range(5000, 10000);
        ov5640_power(sensor, true);
        usleep_range(5000, 10000);

        gpiod_set_value_cansleep(sensor->reset_gpio, 1);
        usleep_range(1000, 2000);

        gpiod_set_value_cansleep(sensor->reset_gpio, 0);
        usleep_range(5000, 10000);
}

static int ov5640_set_power_on(struct ov5640_dev *sensor)
{
        struct i2c_client *client = sensor->i2c_client;
        int ret;

        ret = clk_prepare_enable(sensor->xclk);
        if (ret) {
        dev_err(&client->dev, "%s: failed to enable clock\n",
        __func__);
        return ret;
        }

        ret = regulator_bulk_enable(OV5640_NUM_SUPPLIES,
        sensor->supplies);
        if (ret) {
        dev_err(&client->dev, "%s: failed to enable regulators\n",
        __func__);
        goto xclk_off;
        }

        ov5640_reset(sensor);
        ov5640_power(sensor, true);

        ret = ov5640_init_slave_id(sensor);
        if (ret)
        goto power_off;

        return 0;

power_off:
        ov5640_power(sensor, false);
        regulator_bulk_disable(OV5640_NUM_SUPPLIES, sensor->supplies);
xclk_off:
        clk_disable_unprepare(sensor->xclk);
        return ret;
}

## Step 6: ov5640_s_stream

static int ov5640_s_stream(struct v4l2_subdev *sd, int enable)
{
        struct ov5640_dev *sensor = to_ov5640_dev(sd);
        int ret = 0;

        mutex_lock(&sensor->lock);

        if (sensor->streaming == !enable) {
        if (enable && sensor->pending_mode_change) {
        ret = ov5640_set_mode(sensor);
        if (ret)
        goto out;
        }

        if (enable && sensor->pending_fmt_change) {
        ret = ov5640_set_framefmt(sensor, &sensor->fmt);
        if (ret)
        goto out;
        sensor->pending_fmt_change = false;
        }

        if (sensor->ep.bus_type == V4L2_MBUS_CSI2)
        ret = ov5640_set_stream_mipi(sensor, enable);
        else
        ret = ov5640_set_stream_dvp(sensor, enable);

        if (!ret)
        sensor->streaming = enable;
        }
out:
        mutex_unlock(&sensor->lock);
        return ret;
}

static int ov5640_set_mode(struct ov5640_dev *sensor)
{
        const struct ov5640_mode_info *mode = sensor->current_mode;
        const struct ov5640_mode_info *orig_mode = sensor->last_mode;
        enum ov5640_downsize_mode dn_mode, orig_dn_mode;
        bool auto_gain = sensor->ctrls.auto_gain->val == 1;
        bool auto_exp = sensor->ctrls.auto_exp->val == V4L2_EXPOSURE_AUTO;
        int ret;

        dn_mode = mode->dn_mode;
        orig_dn_mode = orig_mode->dn_mode;

        /* auto gain and exposure must be turned off when changing modes */
        if (auto_gain) {
        ret = ov5640_set_autogain(sensor, false);
        if (ret)
        return ret;
        }

        if (auto_exp) {
        ret = ov5640_set_autoexposure(sensor, false);
        if (ret)
        goto restore_auto_gain;
        }

        if ((dn_mode == SUBSAMPLING && orig_dn_mode == SCALING) ||
        (dn_mode == SCALING && orig_dn_mode == SUBSAMPLING)) {
        /*
        * change between subsampling and scaling
        * go through exposure calculation
        ret = ov5640_set_mode_exposure_calc(sensor, mode);
        } else {
        /*
        * change inside subsampling or scaling
        * download firmware directly
        */
        ret = ov5640_set_mode_direct(sensor, mode);
        }
        if (ret < 0)
        goto restore_auto_exp_gain;

        /* restore auto gain and exposure */
        if (auto_gain)
        ov5640_set_autogain(sensor, true);
        if (auto_exp)
        ov5640_set_autoexposure(sensor, true);

        ret = ov5640_set_binning(sensor, dn_mode != SCALING);
        if (ret < 0)
        return ret;
        ret = ov5640_set_ae_target(sensor, sensor->ae_target);
        if (ret < 0)
        return ret;
        ret = ov5640_get_light_freq(sensor);
        if (ret < 0)
        return ret;
        ret = ov5640_set_bandingfilter(sensor);
        if (ret < 0)
        return ret;
        ret = ov5640_set_virtual_channel(sensor);
        if (ret < 0)
        return ret;

        sensor->pending_mode_change = false;
        sensor->last_mode = mode;

        return 0;

restore_auto_exp_gain:
        if (auto_exp)
        ov5640_set_autoexposure(sensor, true);
restore_auto_gain:
        if (auto_gain)
        ov5640_set_autogain(sensor, true);

        return ret;
}

static int ov5640_set_framefmt(struct ov5640_dev *sensor,
        struct v4l2_mbus_framefmt *format)
{
        int ret = 0;
        bool is_rgb = false;
        bool is_jpeg = false;
        u8 val;

        switch (format->code) {
        case MEDIA_BUS_FMT_UYVY8_2X8:
        case MEDIA_BUS_FMT_UYVY8_1X16:
        /* YUV422, UYVY */
        val = 0x3f;
        break;
        case MEDIA_BUS_FMT_YUYV8_2X8:
        case MEDIA_BUS_FMT_YUYV8_1X16:
        /* YUV422, YUYV */
        val = 0x30;
        break;
        case MEDIA_BUS_FMT_RGB565_2X8_LE:
        /* RGB565 {g[2:0],b[4:0]},{r[4:0],g[5:3]} */
        val = 0x6F;
        is_rgb = true;
        break;
        case MEDIA_BUS_FMT_RGB565_2X8_BE:
        /* RGB565 {r[4:0],g[5:3]},{g[2:0],b[4:0]} */
        val = 0x61;
        is_rgb = true;
        break;
        case MEDIA_BUS_FMT_JPEG_1X8:
        /* YUV422, YUYV */
        val = 0x30;
        is_jpeg = true;
        break;
        default:
        return -EINVAL;
        }

        /* FORMAT CONTROL00: YUV and RGB formatting */
        ret = ov5640_write_reg(sensor, OV5640_REG_FORMAT_CONTROL00, val);
        if (ret)
        return ret;

        /* FORMAT MUX CONTROL: ISP YUV or RGB */
        ret = ov5640_write_reg(sensor, OV5640_REG_ISP_FORMAT_MUX_CTRL,
        is_rgb ? 0x01 : 0x00);
        if (ret)
        return ret;

        /*
        * TIMING TC REG21:
        * - [5]: JPEG enable
        */
        ret = ov5640_mod_reg(sensor, OV5640_REG_TIMING_TC_REG21,
        BIT(5), is_jpeg ? BIT(5) : 0);
        if (ret)
        return ret;

        /*
        * SYSTEM RESET02:
        * - [4]: Reset JFIFO
        * - [3]: Reset SFIFO
        * - [2]: Reset JPEG
        */
        ret = ov5640_mod_reg(sensor, OV5640_REG_SYS_RESET02,
        BIT(4) | BIT(3) | BIT(2),
        is_jpeg ? 0 : (BIT(4) | BIT(3) | BIT(2)));
        if (ret)
        return ret;

        /*
        * CLOCK ENABLE02:
        * - [5]: Enable JPEG 2x clock
        * - [3]: Enable JPEG clock
        */
        return ov5640_mod_reg(sensor, OV5640_REG_SYS_CLOCK_ENABLE02,
        BIT(5) | BIT(3),
        is_jpeg ? (BIT(5) | BIT(3)) : 0);
}

static int ov5640_set_stream_mipi(struct ov5640_dev *sensor, bool on)
{
        int ret;

        /*
        * Enable/disable the MIPI interface
        *
        * 0x300e = on ? 0x45 : 0x40
        *
        * FIXME: the sensor manual (version 2.03) reports
        * [7:5] = 000 : 1 data lane mode
        * [7:5] = 001 : 2 data lanes mode
        * But this settings do not work, while the following ones
        * have been validated for 2 data lanes mode.
        *
        * [7:5] = 010 : 2 data lanes mode
        * [4] = 0 : Power up MIPI HS Tx
        * [3] = 0 : Power up MIPI LS Rx
        * [2] = 1/0 : MIPI interface enable/disable
        * [1:0] = 01/00: FIXME: 'debug'
        */
        ret = ov5640_write_reg(sensor, OV5640_REG_IO_MIPI_CTRL00,
        on ? 0x45 : 0x40);
        if (ret)
        return ret;

        return ov5640_write_reg(sensor, OV5640_REG_FRAME_CTRL01,
        on ? 0x00 : 0x0f);
}

## Step 7: OV5640 SENSOR : [ RESOLUTION, FPS, SCALE(OR)SUBSAMPLING]

### Step 1: Available / Supporting Resolution
enum ov5640_mode_id {
OV5640_MODE_QCIF_176_144 = 0,
OV5640_MODE_QVGA_320_240,
OV5640_MODE_VGA_640_480,
OV5640_MODE_NTSC_720_480,
OV5640_MODE_PAL_720_576,
OV5640_MODE_XGA_1024_768,
OV5640_MODE_720P_1280_720,
OV5640_MODE_1080P_1920_1080,
OV5640_MODE_QSXGA_2592_1944,
OV5640_NUM_MODES,
};

### Step 2: Available / Supporting FPS
enum ov5640_frame_rate {
OV5640_15_FPS = 0,
OV5640_30_FPS,
OV5640_60_FPS,
OV5640_NUM_FRAMERATES,
};

static const int ov5640_framerates [] = {
[OV5640_15_FPS] = 15,
[OV5640_30_FPS] = 30,
[OV5640_60_FPS] = 60,
};

### Step 3: Available / Supporting MEDIA BUS FORMAT
struct ov5640_pixfmt {
u32 code;
u32 colorspace;
};

static const struct ov5640_pixfmt ov5640_formats[] = {
{ MEDIA_BUS_FMT_JPEG_1X8, V4L2_COLORSPACE_JPEG, },
{ MEDIA_BUS_FMT_UYVY8_2X8, V4L2_COLORSPACE_SRGB, },
{ MEDIA_BUS_FMT_YUYV8_2X8, V4L2_COLORSPACE_SRGB, },
{ MEDIA_BUS_FMT_UYVY8_1X16, V4L2_COLORSPACE_SRGB, },
{ MEDIA_BUS_FMT_YUYV8_1X16, V4L2_COLORSPACE_SRGB, },
{ MEDIA_BUS_FMT_RGB565_2X8_LE, V4L2_COLORSPACE_SRGB, },
{ MEDIA_BUS_FMT_RGB565_2X8_BE, V4L2_COLORSPACE_SRGB, },
};

static int ov5640_enum_mbus_code(struct v4l2_subdev *sd,
struct v4l2_subdev_pad_config *cfg,
struct v4l2_subdev_mbus_code_enum *code)
{
if (code->pad != 0)
return -EINVAL;
if (code->index >= ARRAY_SIZE(ov5640_formats))
return -EINVAL;

code->code = ov5640_formats[code->index].code;
return 0;
}

### Step 4: Available / Supporting SCALING / SUBSAMPLING

/*
 * Image size under 1280 * 960 are SUBSAMPLING
 * Image size upper 1280 * 960 are SCALING
 */
enum ov5640_downsize_mode {
SUBSAMPLING,
SCALING,
};

### Step 5: AVAILABLE MODES - STRUCTURE

struct ov5640_mode_info {
enum ov5640_mode_id id;
enum ov5640_downsize_mode dn_mode;
bool scaler; /* Mode uses ISP scaler (reg 0x5001,BIT(5)=='1') */
u32 hact;
u32 htot;
u32 vact;
u32 vtot;
const struct reg_value *reg_data;
u32 reg_data_size;
};

### Step 6: ov5640_dev - STRUCTURE

struct ov5640_dev {
struct i2c_client *i2c_client;
struct v4l2_subdev sd;
struct media_pad pad;
struct v4l2_fwnode_endpoint ep; /* the parsed DT endpoint info */
struct clk *xclk; /* system clock to OV5640 */
u32 xclk_freq;

struct regulator_bulk_data supplies[OV5640_NUM_SUPPLIES];
struct gpio_desc *reset_gpio;
struct gpio_desc *pwdn_gpio;
bool upside_down;

/* lock to protect all members below */
struct mutex lock;

int power_count;

struct v4l2_mbus_framefmt fmt;
bool pending_fmt_change;

const struct ov5640_mode_info *current_mode;
const struct ov5640_mode_info *last_mode;
enum ov5640_frame_rate current_fr;
struct v4l2_fract frame_interval;

struct ov5640_ctrls ctrls;

u32 prev_sysclk, prev_hts;
u32 ae_low, ae_high, ae_target;

bool pending_mode_change;
bool streaming;
};

static int ov5640_get_fmt(struct v4l2_subdev *sd,
 struct v4l2_subdev_pad_config *cfg,
 struct v4l2_subdev_format *format)
{
struct ov5640_dev *sensor = to_ov5640_dev(sd);
struct v4l2_mbus_framefmt *fmt;

if (format->pad != 0)
return -EINVAL;

mutex_lock(&sensor->lock);

if (format->which == V4L2_SUBDEV_FORMAT_TRY)
fmt = v4l2_subdev_get_try_format(&sensor->sd, cfg,
format->pad);
else
fmt = &sensor->fmt;

format->format = *fmt;

mutex_unlock(&sensor->lock);

return 0;
}
struct v4l2_mbus_framefmt { / __u32 width; / __u32 height; / __u32 code; / __u32 field; / __u32 colorspace; / __u16 ycbcr_enc; / __u16 quantization; / __u16 xfer_func; / __u16 reserved[11]; / };

## Step 8: v4l-ctl: sub-dev calls [v4l2-ctrl-subdev.c]

static const struct v4l2_subdev_pad_ops ov5640_pad_ops = {
.enum_mbus_code = ov5640_enum_mbus_code,
.get_fmt = ov5640_get_fmt,
.set_fmt = ov5640_set_fmt,
.enum_frame_size = ov5640_enum_frame_size,
.enum_frame_interval = ov5640_enum_frame_interval,
};

https://linuxtv.org/downloads/v4l-utils/

utils/v4l2-ctrl/v4l2-ctrl-subdev.c

enum_mbus_code	callback for VIDIOC_SUBDEV_ENUM_MBUS_CODE() ioctl handler code.
enum_frame_size	callback for VIDIOC_SUBDEV_ENUM_FRAME_SIZE() ioctl handler code.
enum_frame_interval	callback for VIDIOC_SUBDEV_ENUM_FRAME_INTERVAL() ioctl handler code.
get_fmt	callback for VIDIOC_SUBDEV_G_FMT() ioctl handler code.
set_fmt	callback for VIDIOC_SUBDEV_S_FMT() ioctl handler code.

void subdev_usage(void)
{
printf("\nSub-Device options:\n"
      " --list-subdev-mbus-codes <pad>\n"
      " display supported mediabus codes for this pad (0 is default)\n"
      " [VIDIOC_SUBDEV_ENUM_MBUS_CODE]\n"
      " --list-subdev-framesizes pad=<pad>,code=<code>\n"
      " list supported framesizes for this pad and code\n"
      " [VIDIOC_SUBDEV_ENUM_FRAME_SIZE]\n"
      " <code> is the value of the mediabus code\n"
      " --list-subdev-frameintervals pad=<pad>,width=<w>,height=<h>,code=<code>\n"
      " list supported frame intervals for this pad and code and\n"
      " the given width and height	[VIDIOC_SUBDEV_ENUM_FRAME_INTERVAL]\n"
      " <code> is the value of the mediabus code\n"
      " --get-subdev-fmt [<pad>]\n"
      "	query the frame format for the given pad	[VIDIOC_SUBDEV_G_FMT]\n"

struct v4l2_subdev_video_ops

g_frame_interval	callback for VIDIOC_G_FRAMEINTERVAL ioctl handler code.
s_frame_interval	callback for VIDIOC_S_FRAMEINTERVAL ioctl handler code.

## Step 9: V4L2 – CONTROLS

#include <media/v4l2-ctrls.h>

### Step 1: define the controls
struct ov5640_ctrls {
struct v4l2_ctrl_handler handler;
struct {
struct v4l2_ctrl *auto_exp;
struct v4l2_ctrl *exposure;
};
struct {
struct v4l2_ctrl *auto_wb;
struct v4l2_ctrl *blue_balance;
struct v4l2_ctrl *red_balance;
};
struct {
struct v4l2_ctrl *auto_gain;
struct v4l2_ctrl *gain;
};
struct v4l2_ctrl *brightness;
struct v4l2_ctrl *light_freq;
struct v4l2_ctrl *saturation;
struct v4l2_ctrl *contrast;
struct v4l2_ctrl *hue;
struct v4l2_ctrl *test_pattern;
struct v4l2_ctrl *hflip;
struct v4l2_ctrl *vflip;
};

### Step 2: fill the controls
static const struct v4l2_ctrl_ops ov5640_ctrl_ops = {
.g_volatile_ctrl = ov5640_g_volatile_ctrl,
.s_ctrl = ov5640_s_ctrl,
};

static int ov5640_init_controls(struct ov5640_dev *sensor)
{
const struct v4l2_ctrl_ops *ops = &ov5640_ctrl_ops;
struct ov5640_ctrls *ctrls = &sensor->ctrls;
struct v4l2_ctrl_handler *hdl = &ctrls->handler;
int ret;

v4l2_ctrl_handler_init(hdl, 32);

/* we can use our own mutex for the ctrl lock */
hdl->lock = &sensor->lock;

/* Auto/manual white balance */
ctrls->auto_wb = v4l2_ctrl_new_std(hdl, ops,
  V4L2_CID_AUTO_WHITE_BALANCE,
  0, 1, 1, 1);
ctrls->blue_balance = v4l2_ctrl_new_std(hdl, ops, V4L2_CID_BLUE_BALANCE,
0, 4095, 1, 0);
ctrls->red_balance = v4l2_ctrl_new_std(hdl, ops, V4L2_CID_RED_BALANCE,
      0, 4095, 1, 0);
/* Auto/manual exposure */
ctrls->auto_exp = v4l2_ctrl_new_std_menu(hdl, ops,
V4L2_CID_EXPOSURE_AUTO,
V4L2_EXPOSURE_MANUAL, 0,
V4L2_EXPOSURE_AUTO);
ctrls->exposure = v4l2_ctrl_new_std(hdl, ops, V4L2_CID_EXPOSURE,
   0, 65535, 1, 0);
/* Auto/manual gain */
ctrls->auto_gain = v4l2_ctrl_new_std(hdl, ops, V4L2_CID_AUTOGAIN,
    0, 1, 1, 1);
ctrls->gain = v4l2_ctrl_new_std(hdl, ops, V4L2_CID_GAIN,
0, 1023, 1, 0);

ctrls->saturation = v4l2_ctrl_new_std(hdl, ops, V4L2_CID_SATURATION,
     0, 255, 1, 64);
ctrls->hue = v4l2_ctrl_new_std(hdl, ops, V4L2_CID_HUE,
      0, 359, 1, 0);
ctrls->contrast = v4l2_ctrl_new_std(hdl, ops, V4L2_CID_CONTRAST,
   0, 255, 1, 0);
ctrls->test_pattern =
v4l2_ctrl_new_std_menu_items(hdl, ops,	V4L2_CID_TEST_PATTERN,
    ARRAY_SIZE(test_pattern_menu) - 1,
    0, 0, test_pattern_menu);
ctrls->hflip = v4l2_ctrl_new_std(hdl, ops, V4L2_CID_HFLIP,
0, 1, 1, 0);
ctrls->vflip = v4l2_ctrl_new_std(hdl, ops, V4L2_CID_VFLIP,
0, 1, 1, 0);

ctrls->light_freq =
v4l2_ctrl_new_std_menu(hdl, ops,
      V4L2_CID_POWER_LINE_FREQUENCY,
      V4L2_CID_POWER_LINE_FREQUENCY_AUTO, 0,
      V4L2_CID_POWER_LINE_FREQUENCY_50HZ);

if (hdl->error) {
ret = hdl->error;
goto free_ctrls;
}

ctrls->gain->flags |= V4L2_CTRL_FLAG_VOLATILE;
ctrls->exposure->flags |= V4L2_CTRL_FLAG_VOLATILE;

v4l2_ctrl_auto_cluster(3, &ctrls->auto_wb, 0, false);
v4l2_ctrl_auto_cluster(2, &ctrls->auto_gain, 0, true);
v4l2_ctrl_auto_cluster(2, &ctrls->auto_exp, 1, true);

sensor->sd.ctrl_handler = hdl;
return 0;

free_ctrls:
v4l2_ctrl_handler_free(hdl);
return ret;
}

ret = v4l2_ctrl_handler_setup(&sensor->ctrls.handler);

static int ov5640_g_volatile_ctrl(struct v4l2_ctrl *ctrl)
{
struct v4l2_subdev *sd = ctrl_to_sd(ctrl);
struct ov5640_dev *sensor = to_ov5640_dev(sd);
int val;

/* v4l2_ctrl_lock() locks our own mutex */

/*
* If the sensor is not powered up by the host driver, do
* not try to access it to update the volatile controls.
*/
if (sensor->power_count == 0)
return 0;

switch (ctrl->id) {
case V4L2_CID_AUTOGAIN:
val = ov5640_get_gain(sensor);
if (val < 0)
return val;
sensor->ctrls.gain->val = val;
break;
case V4L2_CID_EXPOSURE_AUTO:
val = ov5640_get_exposure(sensor);
if (val < 0)
return val;
sensor->ctrls.exposure->val = val;
break;
}

return 0;
}

static int ov5640_s_ctrl(struct v4l2_ctrl *ctrl)
{
struct v4l2_subdev *sd = ctrl_to_sd(ctrl);
struct ov5640_dev *sensor = to_ov5640_dev(sd);
int ret;

/* v4l2_ctrl_lock() locks our own mutex */

/*
* If the device is not powered up by the host driver do
* not apply any controls to H/W at this time. Instead
* the controls will be restored right after power-up.
*/
if (sensor->power_count == 0)
return 0;

switch (ctrl->id) {
case V4L2_CID_AUTOGAIN:
ret = ov5640_set_ctrl_gain(sensor, ctrl->val);
break;
case V4L2_CID_EXPOSURE_AUTO:
ret = ov5640_set_ctrl_exposure(sensor, ctrl->val);
break;
case V4L2_CID_AUTO_WHITE_BALANCE:
ret = ov5640_set_ctrl_white_balance(sensor, ctrl->val);
break;
case V4L2_CID_HUE:
ret = ov5640_set_ctrl_hue(sensor, ctrl->val);
break;
case V4L2_CID_CONTRAST:
ret = ov5640_set_ctrl_contrast(sensor, ctrl->val);
break;
case V4L2_CID_SATURATION:
ret = ov5640_set_ctrl_saturation(sensor, ctrl->val);
break;
case V4L2_CID_TEST_PATTERN:
ret = ov5640_set_ctrl_test_pattern(sensor, ctrl->val);
break;
case V4L2_CID_POWER_LINE_FREQUENCY:
ret = ov5640_set_ctrl_light_freq(sensor, ctrl->val);
break;
case V4L2_CID_HFLIP:
ret = ov5640_set_ctrl_hflip(sensor, ctrl->val);
break;
case V4L2_CID_VFLIP:
ret = ov5640_set_ctrl_vflip(sensor, ctrl->val);
break;
default:
ret = -EINVAL;
break;
}

return ret;
}

## Step 10: V4L2 – CONTROLS - TABLE

S.N0	IMP STRUCTURES / FUNCTIONS
1	struct v4l2_ctrl_handler *ctrl_handler; ==in==> struct v4l2_subdev
2	struct v4l2_ctrl_ops { / int (*g_volatile_ctrl)(struct v4l2_ctrl *ctrl); / int (*try_ctrl)(struct v4l2_ctrl *ctrl); / int (*s_ctrl)(struct v4l2_ctrl *ctrl); / };
3	struct v4l2_ctrl { / const struct v4l2_ctrl_ops *ops; / u32 id; / const char *name; / enum v4l2_ctrl_type type; / s64 minimum, maximum, default_value;
4	enum v4l2_ctrl_type { / V4L2_CTRL_TYPE_INTEGER = 1, / V4L2_CTRL_TYPE_BOOLEAN = 2, / V4L2_CTRL_TYPE_MENU = 3, / V4L2_CTRL_TYPE_BUTTON = 4, / V4L2_CTRL_TYPE_INTEGER64 = 5, / V4L2_CTRL_TYPE_CTRL_CLASS = 6, / V4L2_CTRL_TYPE_STRING = 7, / V4L2_CTRL_TYPE_BITMASK = 8, / V4L2_CTRL_TYPE_INTEGER_MENU = 9, / /* Compound types are >= 0x0100 */ / V4L2_CTRL_COMPOUND_TYPES = 0x0100, / V4L2_CTRL_TYPE_U8 = 0x0100, / V4L2_CTRL_TYPE_U16 = 0x0101, / V4L2_CTRL_TYPE_U32 = 0x0102, / };
5	struct v4l2_ctrl *v4l2_ctrl_new_std(struct v4l2_ctrl_handler *hdl, const struct v4l2_ctrl_ops *ops, u32 id, s64 min, s64 max, u64 step, s64 def)
6	struct v4l2_ctrl *v4l2_ctrl_new_std_menu_items(struct v4l2_ctrl_handler *hdl, / const struct v4l2_ctrl_ops *ops, u32 id, u8 _max, / u64 mask, u8 _def, const char * const *qmenu)
7	int v4l2_ctrl_handler_setup(struct v4l2_ctrl_handler *hdl)

V4L2_CTRL_FLAG_VOLATILE:
This control is volatile, which means that the value of the control changes continuously. A typical example would be the current gain value if the device is in auto-gain mode. In such a case the hardware calculates the gain value based on the lighting conditions which can change over time.

## Step 11: APP – V4L2 SUB DEV

### Step 1:
ret = v4l2_async_register_subdev(&sensor->sd);

### Step 2:
drivers/media/v4l2-core/v4l2-subdev.c

const struct v4l2_file_operations v4l2_subdev_fops = {
        .owner = THIS_MODULE,
        .open = subdev_open,
        .unlocked_ioctl = subdev_ioctl,
#ifdef CONFIG_COMPAT
        .compat_ioctl32 = subdev_compat_ioctl32,
#endif
        .release = subdev_close,
        .poll = subdev_poll,
};

static long subdev_ioctl(struct file *file, unsigned int cmd,
        unsigned long arg)
{
        return video_usercopy(file, cmd, arg, subdev_do_ioctl_lock);
}

static long subdev_do_ioctl_lock(struct file *file, unsigned int cmd, void *arg)
{
        struct video_device *vdev = video_devdata(file);
        struct mutex *lock = vdev->lock;
        long ret = -ENODEV;

        if (lock && mutex_lock_interruptible(lock))
        return -ERESTARTSYS;
        if (video_is_registered(vdev))
        ret = subdev_do_ioctl(file, cmd, arg);
        if (lock)
        mutex_unlock(lock);
        return ret;
}

static long subdev_do_ioctl(struct file *file, unsigned int cmd, void *arg)
{
        struct video_device *vdev = video_devdata(file);
        struct v4l2_subdev *sd = vdev_to_v4l2_subdev(vdev);
        struct v4l2_fh *vfh = file->private_data;
#if defined(CONFIG_VIDEO_V4L2_SUBDEV_API)
        struct v4l2_subdev_fh *subdev_fh = to_v4l2_subdev_fh(vfh);
        int rval;
#endif

        switch (cmd) {
        case VIDIOC_QUERYCTRL:
        /*
        * TODO: this really should be folded into v4l2_queryctrl (this
        * currently returns -EINVAL for NULL control handlers).
        * However, v4l2_queryctrl() is still called directly by
        * drivers as well and until that has been addressed I believe
        * it is safer to do the check here. The same is true for the
        * other control ioctls below.
        */
        if (!vfh->ctrl_handler)
        return -ENOTTY;
        return v4l2_queryctrl(vfh->ctrl_handler, arg);

        case VIDIOC_QUERY_EXT_CTRL:
        if (!vfh->ctrl_handler)
        return -ENOTTY;
        return v4l2_query_ext_ctrl(vfh->ctrl_handler, arg);

        case VIDIOC_QUERYMENU:
        if (!vfh->ctrl_handler)
        return -ENOTTY;
        return v4l2_querymenu(vfh->ctrl_handler, arg);

        case VIDIOC_G_CTRL:
        if (!vfh->ctrl_handler)
        return -ENOTTY;
        return v4l2_g_ctrl(vfh->ctrl_handler, arg);

        case VIDIOC_S_CTRL:
        if (!vfh->ctrl_handler)
        return -ENOTTY;
        return v4l2_s_ctrl(vfh, vfh->ctrl_handler, arg);

        case VIDIOC_LOG_STATUS: {
        int ret;

        pr_info("%s: ================= START STATUS =================\n",
        sd->name);
        ret = v4l2_subdev_call(sd, core, log_status);
        pr_info("%s: ================== END STATUS ==================\n",
        sd->name);
        return ret;
        }

#if defined(CONFIG_VIDEO_V4L2_SUBDEV_API)
        case VIDIOC_SUBDEV_G_FMT: {
        struct v4l2_subdev_format *format = arg;

        rval = check_format(sd, format);
        if (rval)
        return rval;

        memset(format->reserved, 0, sizeof(format->reserved));
        memset(format->format.reserved, 0, sizeof(format->format.reserved));
        return v4l2_subdev_call(sd, pad, get_fmt, subdev_fh->pad, format);
        }

        case VIDIOC_SUBDEV_S_FMT: {
        struct v4l2_subdev_format *format = arg;

        rval = check_format(sd, format);
        if (rval)
        return rval;

        memset(format->reserved, 0, sizeof(format->reserved));
        memset(format->format.reserved, 0, sizeof(format->format.reserved));
        return v4l2_subdev_call(sd, pad, set_fmt, subdev_fh->pad, format);
        }

case VIDIOC_SUBDEV_ENUM_MBUS_CODE: {
        struct v4l2_subdev_mbus_code_enum *code = arg;

        if (code->which != V4L2_SUBDEV_FORMAT_TRY &&
        code->which != V4L2_SUBDEV_FORMAT_ACTIVE)
        return -EINVAL;

        if (code->pad >= sd->entity.num_pads)
        return -EINVAL;

        memset(code->reserved, 0, sizeof(code->reserved));
        return v4l2_subdev_call(sd, pad, enum_mbus_code, subdev_fh->pad,
        code);
        }

        case VIDIOC_SUBDEV_ENUM_FRAME_SIZE: {
        struct v4l2_subdev_frame_size_enum *fse = arg;

        if (fse->which != V4L2_SUBDEV_FORMAT_TRY &&
        fse->which != V4L2_SUBDEV_FORMAT_ACTIVE)
        return -EINVAL;

        if (fse->pad >= sd->entity.num_pads)
        return -EINVAL;

        memset(fse->reserved, 0, sizeof(fse->reserved));
        return v4l2_subdev_call(sd, pad, enum_frame_size, subdev_fh->pad,
        fse);
        }

        case VIDIOC_SUBDEV_ENUM_FRAME_INTERVAL: {
        struct v4l2_subdev_frame_interval_enum *fie = arg;

        if (fie->which != V4L2_SUBDEV_FORMAT_TRY &&
        fie->which != V4L2_SUBDEV_FORMAT_ACTIVE)
        return -EINVAL;

        if (fie->pad >= sd->entity.num_pads)
        return -EINVAL;

        memset(fie->reserved, 0, sizeof(fie->reserved));
        return v4l2_subdev_call(sd, pad, enum_frame_interval, subdev_fh->pad, fie);
        }

### Step 3:

int v4l2_device_register_subdev_nodes(struct v4l2_device *v4l2_dev)

        struct video_device *vdev;
        struct v4l2_subdev *sd;
        int err;

        /* Register a device node for every subdev marked with the
        * V4L2_SUBDEV_FL_HAS_DEVNODE flag.
        */
        list_for_each_entry(sd, &v4l2_dev->subdevs, list) {
        if (!(sd->flags & V4L2_SUBDEV_FL_HAS_DEVNODE))
        continue;

        if (sd->devnode)
        continue;

        vdev = kzalloc(sizeof(*vdev), GFP_KERNEL);
        if (!vdev) {
        err = -ENOMEM;
        goto clean_up;
        }

        video_set_drvdata(vdev, sd);
        strlcpy(vdev->name, sd->name, sizeof(vdev->name));
        vdev->v4l2_dev = v4l2_dev;
        vdev->fops = &v4l2_subdev_fops;
        vdev->release = v4l2_device_release_subdev_node;
        vdev->ctrl_handler = sd->ctrl_handler;
        err = __video_register_device(vdev, VFL_TYPE_SUBDEV, -1, 1, sd->owner);
        if (err < 0) {
        kfree(vdev);
        goto clean_up;
        }
        sd->devnode = vdev;

### Step 4:

drivers/media/v4l2-core/v4l2-dev.c

int __video_register_device(struct video_device *vdev,
        enum vfl_devnode_type type,
        int nr, int warn_if_nr_in_use,
        struct module *owner)
{
        int i = 0;
        int ret;
        int minor_offset = 0;
        int minor_cnt = VIDEO_NUM_DEVICES;
        const char *name_base;

/* Part 1: check device type */
        switch (type) {
        case VFL_TYPE_GRABBER:
        name_base = "video";
        break;
        case VFL_TYPE_VBI:
        name_base = "vbi";
        break;
        case VFL_TYPE_RADIO:
        name_base = "radio";
        break;
        case VFL_TYPE_SUBDEV:
        name_base = "v4l-subdev";
        break;
        case VFL_TYPE_SDR:
        /* Use device name 'swradio' because 'sdr' was already taken. */
        name_base = "swradio";
        break;
        case VFL_TYPE_TOUCH:
        name_base = "v4l-touch";
        break;
        default:
        pr_err("%s called with unknown type: %d\n",
        __func__, type);
        return -EINVAL;
        }

        vdev->vfl_type = type;
        vdev->cdev = NULL;

/* Part 2: find a free minor, device node number and device index. */
#ifdef CONFIG_VIDEO_FIXED_MINOR_RANGES
        /* Keep the ranges for the first four types for historical
        * reasons.
        * Newer devices (not yet in place) should use the range
        * of 128-191 and just pick the first free minor there
        * (new style). */
        switch (type) {
        case VFL_TYPE_GRABBER:
        minor_offset = 0;
        minor_cnt = 64;
        break;
        case VFL_TYPE_RADIO:
        minor_offset = 64;
        minor_cnt = 64;
        break;
        case VFL_TYPE_VBI:
        minor_offset = 224;
        minor_cnt = 32;
        break;
        default:
        minor_offset = 128;
        minor_cnt = 64;
        break;
        }

/* Part 3: Initialize the character device */
        vdev->cdev = cdev_alloc();
        if (vdev->cdev == NULL) {
        ret = -ENOMEM;
        goto cleanup;
        }
        vdev->cdev->ops = &v4l2_fops;
        vdev->cdev->owner = owner;
        ret = cdev_add(vdev->cdev, MKDEV(VIDEO_MAJOR, vdev->minor), 1);
        if (ret < 0) {
        pr_err("%s: cdev_add failed\n", __func__);
        kfree(vdev->cdev);
        vdev->cdev = NULL;
        goto cleanup;
        }

       /* Part 4: register the device with sysfs */
        vdev->dev.class = &video_class;
        vdev->dev.devt = MKDEV(VIDEO_MAJOR, vdev->minor);
        vdev->dev.parent = vdev->dev_parent;
        dev_set_name(&vdev->dev, "%s%d", name_base, vdev->num);
        ret = device_register(&vdev->dev);
        if (ret < 0) {
        pr_err("%s: device_register failed\n", __func__);
        goto cleanup;
        }
        /* Register the release callback that will be called when the last
        reference to the device goes away. */
        vdev->dev.release = v4l2_device_release;

        if (nr != -1 && nr != vdev->num && warn_if_nr_in_use)
        pr_warn("%s: requested %s%d, got %s\n", __func__,
        name_base, nr, video_device_node_name(vdev));

        /* Increase v4l2_device refcount */
        v4l2_device_get(vdev->v4l2_dev);

        /* Part 5: Register the entity. */
        ret = video_register_media_controller(vdev);

        /* Part 6: Activate this minor. The char device can now be used. */
        set_bit(V4L2_FL_REGISTERED, &vdev->flags);

4l2_async_register_subdev