CSI Host and Image Sensor(OV5640) configuration

1. Three trust zones are disabled to save the captured images from sensor on DDR.
2. Powered up the CSI (Display sub system) from system control Register
3. Specified the number of MIPI lanes as 2
4. De-asserted D-PHY shutdown, D-PHY reset and CSI reset.
5. Number of Buffer descriptors are configured as 10
6. Resolution is configured as 640x480
7. Pixel format, endianess, data type are configured.
8. Interrupt is configured to generate after 10 frames are captured.
9. Interrupts are enabled to track the errors.
10. Bit Rate of the CSI -PHY is configured as 224, which is double of the MIPI Clock configured in OV5640. (Optional).
11. Finally configured the OV5640 camera registers with the values, which is provided by Omni- vision.
12.Here some registers related to MIPI clock and pixel format have been modified to configure it for RGB565 and RGB888.
13. RGB565 and RGB888 are working at MIPI clock 112MHz.
14. Format Control Register (Address at 0x4300) configured as 0x60 for RGB565.
15. Format Control Register (Address at 0x4300) configured as 0x20 for RGB888.
16. To test the color pattern, PRE ISP TEST SETTING 1 Register (at address 503D) configured as 0x80.
17. Then started the stream on by configuring FRAME CTRL02 Register (at address 0x4202) as 0x00.
18. Started to store the captured frames into DDR after the interrupt is generated which is configured in CSI2_BRIDGE_FRAME_INTNUM_VC1 register in CSI bridge.
19. Tested the streaming on HDMI, CLCD and DSI by copying and converting the captured data in CSI buffer descriptor location to HDMI, CLCD and DSI buffer descriptor locations.

Color issue with RGB888 Format:
When pixel format RGB565 is configured in OV5640, we can see the proper images on display devices. But display devices like HDMI and DSI are configured for RGB888. So, we need to convert image data from RGB888 to RGB565 manually pixel by pixel. It becomes streaming much slow and is not proper on display.

In case of YUV4:2:0 or YUV4:2:2 pixel formats, we don't have configuration settings for these from OminiVision.
HDMI bridge supports only planar format (All Y, U and V component separately).OV5640 supports only non-planar format ( All Y, U and V component packed together). But CSI bridge supports both planar and non-planar. There is bit YUV Data Alignment(7th bit) in Frame Format Configuration Register in CSI bridge to configure planar format, even non-planar data came form OV5640 sensor. But here the problem is we need to copy 3 components (Y,U,V) in each frame from CSI to HDMI frame buffer. So, again there is delay in streaming on display devices. So, thats what finally we have chosen RGB 888.

Planar Format:

While streaming on all the display devices like HDMI, CLCD and DSI, there is color issue with RGB888. To resolve this we have found some observations and done some configuration changes, find those below. But it couldn't be resolved.

Observations:
1. No full resolution support for RGB888 mentioned in OV5640 data sheet.
2. No configuration code is available for RGB888 in INTERNET.
3. Most of the teams from different Orgs tested for RGB565, YUV422.

Configuration Changes:
1. Modified MIPI clock in OV5640 between112MHz and 180MHz with 10MHz difference.
2. By enabling and disabling the binning and skipping sub sampling modes.